## Slide 1
SRv6 L3VPN, shown on real boxes
A whiteboard session with proof: seven VyOS routers, two tenants, one packet followed hop by hop
fd00:c
block · 32 bits
11
p1
13
p3
3
pe3
e001
uDT4 · tenant-b
::
one address, five instructions — the whole session in a line
Notes: Open with the address. Every part of the session explains one slot of it.

## Slide 2
Why SRv6: the instructions move into the address
What an SRv6 core does not have
0
label tables, LDP, RSVP —
no signalling protocol for transport
1
extra header: IPv6
(and often no SRH at all)
0
per-tunnel state in the core —
P routers only route IPv6
A SID is an address that means "do this when you own me". End = forward. End.X = out this link. End.DT4 = strip the IPv6 header and look the inner IPv4 packet up in this VRF. A router that does not own the address just routes IPv6 — that is the entire core.
Notes: 5 minutes. The single idea. Everything else follows.

## Slide 3
The lab
4 data centres · 3 P routers · 2 tenants · 19 VMs on one host
VyOS rolling (FRR 10.6, Linux 6.18) · IS-IS L2, IPv6-only, MTU 9000 · uSID fd00:c::/32 · reflectors p1 + p3 · BFD everywhere · Alpine hosts
Notes: Whiteboard 1 starts here: draw the triangle and the four lanes.

## Slide 4
A locator is a prefix; a SID is an instruction inside it
Whiteboard 1 — uSID structure f3216: block 32 bits · node 16 · function 16
fd00:c
block
3
node: pe3
e000
function: End.DT4, tenant-a
::
zeros
fd00:c:3::/48 pe3's locator, advertised in IS-IS like any prefix
fd00:c:3:e000:: pe3's End.DT4 for tenant-a (allocated by FRR at run time)
fd00:c:3:e002::/64 an End.X: out pe3's eth1, to p2
What IS-IS carries
The /48 (an ordinary prefix) plus SRv6 sub-TLVs: how deep an SRH the node can process (SRH Max SL 3), how many segments it can push. Nothing new on the wire.
What the kernel holds
seg6local routes on the owner only: End (uN) for the /48, one End.X (uA) per adjacency, one End.DT4 per tenant VRF on a PE. A P router has exactly the first two kinds.
Notes: Live: show isis neighbor; show ipv6 route isis | grep fd00:c:; ip -6 route show | grep seg6local on p2 and pe1.

## Slide 5
Three instructions are enough for an L3VPN
Each is one seg6local route on the node that owns the address
behaviour | example SID | meaning | installed by | where
End (uN) | fd00:c:12::/48 | shift the next uSID into place and forward | isisd | every core node
End.X (uA) | fd00:c:12:e003::/64 | forward out this adjacency, regardless of the IGP | isisd | every core link
End.DT4 (uDT4) | fd00:c:1:e001:: | decapsulate; route the inner IPv4 packet in VRF tenant-a | bgpd (sid vpn export auto) | PEs, one per tenant
The non-textbook part. Linux scopes the SRv6 encapsulation's outer lookup to the ingress VRF for forwarded packets. Without a route to the remote locator inside the tenant table, every encapsulated packet is dropped (Ip6OutNoRoutes). The renderer leaks each locator into each VRF via the attached P routers on the IGP shortest path, plus the whole block as a fallback. You only learn this by building it.
Notes: Act 1 ends here. Expect 'where is the tunnel?' — there is none.

## Slide 6
The overlay is the BGP VPN you already know
Whiteboard 2 — a SID where the label used to be
pe1
VRF tenant-a · tenant-b
pe3
VRF tenant-a · tenant-b
p1 · RR
fd00:a::11
p3 · RR
fd00:a::13
VPNv4 over IPv6 loopback sessions (extended next hop), every PE to both reflectors
RD 65000:103 : 172.20.3.0/24 RT:65000:100 Originator 10.255.0.3, Cluster list 10.255.0.11
Remote SID: fd00:c:3:: sid structure=[32 16 16 0 16 48] Remote labels: 917504
917504 = 0xE000 << 4: the 16 function bits are transposed into the label field; the receiver reassembles fd00:c:3:e000::
Unchanged
RD, RT, reflectors, import/export policy, eBGP to the CE inside the VRF.
Changed
The transport attribute: Prefix-SID instead of a label. No LFIB anywhere.
Redundant
Two copies of every route, one per reflector; losing p1 changes nothing (suite 06).
Notes: Live: show bgp ipv4 vpn summary; show bgp ipv4 vpn 172.20.3.0/24 on pe1.

## Slide 7
What the PE actually installs
No label table — a VRF route that says "wrap in IPv6 to this address"
vyos@pe1:~$ ip route show vrf tenant-a
172.20.3.0/24 nhid 96 encap seg6 mode encap segs 1 [ fd00:c:3:e000:: ] via inet6 fe80::…:603 dev eth2 proto bgp
172.20.2.0/24 nhid 82 proto bgp
nexthop encap seg6 mode encap segs 1 [ fd00:c:2:e001:: ] via … dev eth1 weight 1
nexthop encap seg6 mode encap segs 1 [ fd00:c:2:e001:: ] via … dev eth2 weight 1
One segment
The destination address is the whole instruction: pe3's End.DT4 for tenant-a. Out eth2 because pe3's locator is shortest via p2.
ECMP for free
The dc2 LAN has two next hops: pe2 is equidistant via p1 and p2. Nothing configured — it falls out of the IGP.
The CE sees nothing
Plain eBGP routes from its PE. No SRv6, no IPv6, no idea there is a core.
Notes: Act 2 ends. Then act 3: the capture.

## Slide 8
Packet walk: dc1-h1 → dc3-h1
Captured on p2, the router in the middle
dc1-h1
172.20.1.2
ce1
IPv4
pe1
encap
p2
IPv6 lookup
pe3
End.DT4
ce3
IPv4
dc3-h1
172.20.3.2
IPv6 fd00:a::1 → fd00:c:3:e000:: + SRH (1 entry)
vyos@p2:~$ sudo tcpdump -ni eth5 -vv 'ip6 and dst net fd00:c:3::/48'
IP6 (hlim 62, next-header Routing (43)) fd00:a::1 > fd00:c:3:e000::: RT6 (len=2, type=4, segleft=0, [0]fd00:c:3:e000::)
IP (ttl 63) 172.20.1.2 > 172.20.3.2: ICMP echo request
hlim 62
two routers decremented it: pe1 and p2
inner ttl 63
only ce1 touched it — the core is invisible to the tenant's traceroute
isolation
dc1-h1 → dc1-h2 (tenant-b, same site): 100 % loss. No route, no firewall.
Notes: Act 3 live. Ping, capture, traceroute, the failed cross-tenant ping.

## Slide 9
uSID: the whole path in one address
Whiteboard 3 — shift-and-forward (uN with the NEXT-C-SID flavour)
fd00:c
block
11
p1
13
p3
3
pe3
e001
uDT4 · tenant-b
::
leaves pe1
fd00:c:11:13:3:e001::
the carrier: p1 is first after the block, so p1 owns it
leaves p1
fd00:c:13:3:e001::
p1 deleted its own ID and shifted 16 bits left
leaves p3
fd00:c:3:e001::
down to pe3's uDT4 — exactly what an unsteered packet carries
Captured live on p1's link to p3 and on p3's link to pe3 (act 4). The SRH still shows the original carrier; segments-left stays 0.
Notes: This is the slide people remember. Then act 4.

## Slide 10
Steering: uSID carrier vs. an SRH
The same explicit path pe1 → p1 → p3 → pe3 two ways
uSID carrier (default)
encap seg6 segs 1
[ fd00:c:11:13:3:e001:: ]
• 1 segment, a one-entry SRH (24 B), none with reduced encapsulation
• P routers only rewrite the destination address
• no per-path state anywhere in the core
• measured ~120 Mbit/s on a 1-vCPU software data plane
Uncompressed SRH (--uncompressed)
encap seg6 segs 3
[ fd00:c:11:: fd00:c:13::
fd00:c:3:e001:: ]
• 3 × 128-bit segments: a 56-byte SRH
• every hop processes the SRH (segments-left)
• also works here — within a few percent of the carrier
• what uSID was designed to avoid at scale
Steering is unidirectional: the return path takes the IGP shortest path through p2 unless steered too. tools/steer.py add | del — the portal has the same button.
Notes: Contrast slide. Point at the byte counts.

## Slide 11
Failover: a silent link failure
Act 5 — firewall drops IS-IS and BFD on p2's link to pe3; the interface stays up
300 ms × 3
BFD interval and multiplier on every core adjacency
≈ 1 s
detection + SPF + FIB: pe3 moves every tenant route to p3
4 / 150
packets lost at 0.2 s spacing across cut and repair (suite 08: ≤ 10)
pe3 isisd: %ADJCHANGE: Adjacency to p2 (eth1) for level-2 changed from Up to Down, bfd session went down
Without BFD
30-second IS-IS hold time: half a minute of black hole with the link light on.
Nothing in BGP moves
The VPN routes still point at the same SIDs; only the IGP path to the locator changed.
Seen three ways
Grafana annotation region, the router's syslog line, the log-derived alert.
Notes: Run act 5 while talking. Say: interfaces stay up, watch the ping count.

## Slide 12
Operated like a network, not a demo
Act 6 — everything around the seven routers
1
Source of truth
Nautobot models sites, devices, links, VRFs / RTs / RDs, peerings, locators. One renderer produces every config from Nautobot or from lab.conf — a test proves they agree, line for line.
2
Provisioning
A portal adds a tenant or a site as a pipeline: allocate, model, render, boot, push, test, back up to Gitea — each step's log on the page. Removal is the same pipeline in reverse.
3
Verification
64 Robot Framework cases: underlay, SIDs, VPN, isolation, reflector loss, steering, BFD failover, throughput, Nautobot, monitoring. Results with configs and routing tables are committed.
4
Telemetry
Pulled (node-/frr-exporter) and pushed (VyOS Telegraf) metrics into VictoriaMetrics; syslog into VictoriaLogs with log-derived alerts; sFlow from the core; Grafana with annotated events.
Notes: Show render --check, the portal state, one Grafana dashboard, the flows.

## Slide 13
What you only learn by building it
Four things not in the textbook
Linux scopes the outer lookup
Encapsulated packets need a route to the remote locator inside the ingress VRF. Leak the locators per VRF, IGP-consistently, or traffic silently dies (Ip6OutNoRoutes).
uSID needs a /128 anchor
A connected /48 on the dummy interface outranked the uN route in zebra; the node stopped shifting. A /128 keeps the interface up and lets IS-IS own the /48.
Silence is the hard failure
Admin-disabling a link tells the neighbour. The failure that matters is the one only BFD sees — and this build left a stuck BFD session on a disabled interface.
Routers do not log by default
VyOS renders FRR at 'notifications'; %ADJCHANGE is informational. A failover left no syslog until the level was raised and log-neighbor-changes set per VRF.
Notes: Good interview material: each of these is a 'tell me about a time you debugged something' story.

## Slide 14
Run it yourself
git clone https://github.com/dcantor/srv6-core
./lab.sh up && ./lab.sh bootstrap && ./lab.sh test
docs/srv6-walkthrough.pdf — the long-form version with every capture
docs/session/ — this session: guide, questions, exercises
tools/demo_live.py — the six acts, presenter mode
lab-portal/monitoring — the telemetry stack for every lab
VyOS · FRR · Nautobot · Robot Framework · Prometheus · VictoriaMetrics · VictoriaLogs · Grafana · goflow2
Notes: Hand out the walkthrough PDF and the question bank.